## Slide 1: EagleSat Flight Operations
Mo Sabliny
Dr. Yale
Arizona Space Grant Symposium
April 12, 2014

## Slide 2: EagleSat
EagleSat is ERAU Prescott’s first satellite program
Developed by undergraduate students and mentors
Mission
  Measure orbital decay
  Solar radiation effects on CPU memory

## Slide 3: Flight Operations Objective
Determine the orbital model
  Eclipse calculations
  Pass times
  Predict orbital decay
  Calculate radiation and effects
  Develop a mission timeline
  Develop a best fit orbital decay model from data (post flight)

## Slide 4: Flight Dynamics
STK allows for quick results by entering multiple initial conditions
MATLAB allows for an in depth analysis of an orbit
Use for both STK and MATLAB for accuracy
STK vs. MATLAB

## Slide 5: STK Results
Classical Orbital Elements
Orbital Element | Value
Semi-Major Axis (km) | 6795.746
Eccentricity | 0.000281
Inclination(deg) | 51.652
Argument of Perigee (deg) | 37.68
RAAN (deg) | 222.166
Mean Anomaly (deg) | 302.797

## Slide 6: STK Results
Earth
Percentage in Sun and Eclipse

## Slide 7: STK Results
Downlink Opportunities
  About 60 opportunities per week
  Shortest: 3.75 minutes
  Longest: 8.67 minutes
  About 38 opportunities per week during school hours

## Slide 8: MATLAB Orbit Propagation
Utilize ode45 function with a few possible models
  Relative 2-Body problem
    Assumes Earth doesn’t rotate
    Assumes Earth is spherical
  Non-spherical Earth 2-Body problem
  N-body problem
    Takes into account gravitational effects of nearby bodies
Propagating the state vector through each time step
  State vector is the position and velocity vector {x,y,z,vx,vy,vz}
  Calculate the differential state vector {vx,vy,vz,ax,ay,az}

## Slide 9: Eclipse Calculations
Umbra
Penumbra
Antumbra
Sun
Earth
θe
θu
θp
rsat/e
re/s
Rs
Re
EagleSat
hu
Θe = cos-1((rsat/e·re/s)/(rsat/e*re/s))
Θu = tan-1(Re/hu)
Θp = π – tan-1(re/s/(Rs + Re)
du = ((hu * sin(Θu))/sin(Θe + Θu)) = distance to umbra cone edge along satellite

## Slide 10: Eclipse Calculations
These calculations determine where the satellite is in ecliptic terms
  Umbra -Total Eclipse (No Sun)
  No Eclipse (Full Sunlight)
  Penumbra, Antumbra - Partial Eclipse (Fraction of the Sun)
    Further calculations to calculate the fraction of the Sun the satellite sees

## Slide 11: Passes
Earth
rSAT/GS= {S;E;Z}
EagleSat
Ground Station
θE
When θE is greater that 0°, and less than 180° the satellite can be “seen”
Not always the case, when land formations, buildings, etc. are taken into account
θE = sin-1(Z/rSAT/GS)

## Slide 12: Future Work
Effects of Radiation on lifetime of satellite:
  Solar Radiation, Earth Radiation, Earth Albedo
Attempt to model orbital decay
Establish a mission timeline that will incorporate each aspect of the orbital model
Determine a model to best fit data from flight
  Statistical Determination

## Slide 13: Conclusion
These different aspects of an orbital model contribute to the development of a mission timeline
Prepares the EagleSat team for what to expect when considering everything that can affect the satellite

## Slide 14: Acknowledgements
Mentors:
Dr. Gary Yale
Dr. John Post
Jack Crabtree
Organizations:
Arizona Space Grant Consortium
Ignite

## Slide 15: Questions?
Thank you.