## Slide 1
Solar Power for High-Altitude Balloon Payloads
Nathaniel Faint, Henry Luna, Attalie Faint, Moriah Faint
Central
Arizona
College

## Slide 2: Fall 2015
Used small solar panel to successfully recharge digital camera battery.
Flew Basic Stamp & collected valid data from its sensors.
Payload weight: 0.8 lbs.

## Slide 3: Spring 2016 Objectives
Power Basic Stamp with solar panels.
Correlate power produced by panels to available light with a separately powered Arduino system.
Gather GPS data during flight.
Capture high-quality video with lightweight camera (we chose the Mobius Actioncam).

## Slide 4: Payload Construction
Enclosure design was based on solar panel size.
Solar array consisted of 6 thin-film panels wired in parallel (this adds amperage).
Camera was mounted facing down.
Payload weighed 1.27 lbs.

## Slide 5: Payloads
Last semester...
This semester

## Slide 6: Measuring Solar Efficiency
Light sensor measured luminosity (in lux).
In-line current sensor measured volts and amps from solar array.
The two sensors would have enabled us to compare available light to power output from solar array.

## Slide 7: Arduino System
Arduino Mega
SD Shield
GPS
9 DOF
Pressure
Ambient Light
Current

## Slide 8: Flight Results
Basic Stamp took four data readings then failed due to software issues.
Current sensor also gave faulty data.
All other data were valid.
Mobius camera recorded clear video.

## Slide 9: Flight Data Graph

## Slide 11: Conclusions
Solar panels will provide power comparable to a heavy battery.
Solar power is a great way to conserve weight and space on a payload.
The Mobius is a good lightweight camera option.

## Slide 13
Arizona Space Grant Consortium
Our Professors: Tammy Janisko & Dr. Pryor
Mr. Crabtree & ANSR Volunteers
Fellow Students
Paul McWhorter at toptechboy.com
Jeremy Blum at jeremyblum.com
Adafruit.com
Acknowledgments:
https://sites.google.com/site/stratoseekersascendfall2015/home

## Slide 14
Thank You!