## Slide 1: High Altitude Ballooning Communication Stability
Greg Wilburn
Rolfe Bode
Susan Brew
University of Arizona, Tucson, AZ
16 April 2016

## Slide 2: Why Ballooning?
Scientific research:
  Telescopes
  Weather/ atmosphere data
Low space tourism
All done at much lower costs than traditional methods

## Slide 3: Voyager Capsule
Voyager Capsule picture

## Slide 4: The Problem
Must communicate with balloons 100,000 feet in air
4 YAGI antennas mounted to ground based Mobile Command Center (MCC)
Without reliable mounting, significant data may be lost
  Needed for sensitive missions
Previous solution broke down

## Slide 5: Objectives
Design stable antenna mounting system to communicate with balloons
Includes updating existing infrastructure and designing new system

## Slide 6: Methods
Define Requirements
Research existing solutions
Create preliminary design in SolidWorks
Preliminary Design Review (PDR) to engineers at World View
Finalize design and cost report

## Slide 7: Final Design
2 galvanized square steel tubes
  Inner tube: 2.25”x2.25”x3’
  Outer tube: 2.5”x2.5”x1.5’
2 A36 steel plates
  Top plate: 6”x6”x.25”
  Bottom plate: 12”x12”x.1875”
Slide inner tube into bottom prior to each flight

## Slide 8: Final Design (cont’d)
Bottom tube remains mounted to MCC infrastructure
Deflection of .294”
  Under max wind load of 60 mph
  Angle of deflection: .618o

## Slide 9: An Engineering Learning Experience
Keep It Simple, Stupid
Decided on straightforward, cost effective design
COTS solutions far too expensive for the appllication

## Slide 10: THANK YOU!
With special thanks to my mentor, Rolfe Bode, and engineers Zane Maccagnano, Tim Basta and Kyler Felton