## Slide 1: Wayfarer: On-Demand Solar System Exploration with a Common Architecture CubeSat
Matthew Prevallet
4/26/16
Arizona/NASA Space Grant Symposium

## Slide 2: Problem
Current methods slow and costly
Inner solar system celestial objects under categorized
Forbes.com
Space.com, March 28th
Notes: Current methods for exploring space extremely costly and slow to respond
No on demand survey missions: target selected well before launch
Inner solar system celestial objects under categorized

## Slide 3: Objective
Develop framework for general purpose Nano-satellite
Fleet in parking orbit, waiting for a task
Proof of concept: Schwassmann–Wachmann 3
Notes: General purpose rapi response Nano-satellite
Fleet in parking orbit, waiting for a task
Proof of concept: for CubeSat rendezvous with comet Schwassmann–Wachmann 3
Technology Demonstration
Science

## Slide 4: What is a CubeSat?
Miniature satellite
1U of volume = 10 x 10 x 10 cm3
6U = 30 x 20 x 10 cm3
Ridesharing capability
Relatively new technology
Low Cost
University of Tokyo Cubesat
MarCO
Notes: Miniature satellite
1U of volume = 10 x 10 x 10 cm3
6U = 30 x 20 x 10 cm3
Rideshare options
Relatively new technology
Low Cost

## Slide 5: Design Approach
Constraints:
Volume: 6U
Mass: 14 kg
Power: 55 Watts
Cost: Approx. $5-6 million
Subsystems/Trade Studies:
Power
Propulsion
Communications
Attitude Determination
Torquing
Thermal
Notes: Budgets for cost, mass, volume and power
Volume: 6U, Mass: 14 kg, Power: 55 Watts, Cost: Approx. 5-6 million US Dollars,
Subsystems/Trade Studies: Power, Propulsion, Communications, Attitude Determination, Orbital Requirements, Torquing, Thermal

## Slide 6: Power
Power of Required: 55 (Watts)
Distance from Sun: max 1.3 AU
Manufacturer: Clyde Space
Panels: ~200 W/m2
Area Needed: 0.284 m2
Notes: Actual panel will fold up, the one above is a non folding panel.
Talk about, how part was chose, why it was chose

## Slide 7: Propulsion
Busek BIT-3 Engine
Ion Propulsion
50 Watts needed
High efficiency, ~3500 sec ISP
20,000 hour lifetime
Iodine propellant
2.5 kg of fuel needed
Notes: Details about specifications, why these are auditable for mission, why they are the best choice
Iodine propellant, does not have to be as pressurized and is higher density than Xenon - so takes up less space, and lighter storage apparatus can be used
http://www.clyde-space.com/cubesat_shop/solar_panels/6u_solar_panels/335_6u-cubesat-side-solar-panel

## Slide 8: Thermal
1.5 AU with engine off → 1 AU with engine on
Solar Panels: -5 to 55 C
Body of CubeSat: -57 to 10 C
Battery will have heating system
Notes: Next Steps:
Use FEA software
Energy output particular parts

## Slide 9: Next Steps
Finalize trade study results
Write detailed proposal based on our research

## Slide 10: Thank You!
Dr. David Gaylor
NASA Space Grant & Arizona Space Grant Consortium