## Slide 1: ASCEND! Team – Spring 2017
Nicholas Mallott, mallottn@erau.edu
Embry-Riddle Aeronautical University, Prescott
ASCEND! Team Lead
Arizona Space Grant Consortium – 4.22.2017 Symposium

## Slide 2: Team Members
Nicholas Mallott – Aerospace Engineering Student
  Team Lead, Structural Design and Integration
Xander Pickard – Mechanical Engineering Student
  Fabrication and Lead Technologist
Jack Crabtree - Mentor

## Slide 3: Table of Contents
Problem Statement
Objectives
General Principles
Payload Design
Implementation
Results (Fall + Spring Launches)
Comparative Analysis
Conclusions / Takeaways

## Slide 4: Problem Statement
Balloon controllability
Axial spin / tilt in flight
Rates of acceleration
Rates of spin

## Slide 5: Objectives
Develop a passive control system
Design a system to reduce axial rotation rates
Prevent tilt of system about secondary axes
Reduce acceleration spikes
Build a system to accomplish this using aerodynamic principles

## Slide 6: General Principles
Airfoil Designs
  Joukovsky 18% Symmetrical Airfoil
  Joukovsky 15% Symmetrical Airfoil
  Eppler 479 Aerobatic Airfoil
Mass-moment of inertia
Flutter vs Airfoil Design
  Function of Structure, Inertia and Applied Aerodynamic Forces

## Slide 7: Payload Design
ABS (acrylonitrile butadiene styrene) plastic main chassis for sensors / base
  Stronger, flexible and accuracy
PLA (polylactic acid) for outrigger system
  Lighter, higher rigidity and softer rounding edges
Zinc rods for connectors
Fiberglass center rod
Razor IMU (9-axis sensor)

## Slide 8: Results (Fall Launch)

## Slide 9: Results (Fall Launch)
Average Ascent Spin = 17.02 degrees per second

## Slide 10: Results (Spring Launch)

## Slide 11: Results (Spring Launch)
Average Ascent Spin = 4.32 degrees per second

## Slide 12: Comparative Analysis
Accelerometer Data:
  Less “noise” throughout ascent
  Reduced number of data spikes
Gyroscope Data:
  Average spin rate decreased by factor of ~4.25
  Noise reduced and spikes reduced significantly

## Slide 13: Conclusions / Takeaways
Effective at reduction of spin rates
Reduction of noise in accelerometer and gyroscope data – stabilization of change in rates
Effective for creating a stable platform for additional testing
Eclipse flight on 4/15
implementing design
Potential for control
usage on future flights

## Slide 14: Acknowledgements
The Arizona Space Grant Consortium for the support, vision and opportunity to enable this project to carry on
Arizona Near-Space Research for their support of and for the ASCEND! Project, and for their dedication to science and exploration
Embry-Riddle Aeronautical University for their pursuit of excellence, in and out of the classroom
Prof. Jack Crabtree for his continued support, guidance and supervision of this project

## Slide 15: Questions?
Thank you for your support and your time.

## Slide 16: Questions?
Thank you for your support and your time.

## Slide 17: Images taken from:
https://theta360.com/en/about/theta/s.html
http://www.ansr.org/
https://www.nasa.gov/
http://spacegrant.pr.erau.edu/
https://spacegrant.arizona.edu/
http://www.airfoiltools.com/airfoil/details?airfoil=e479-il
http://www.airfoiltools.com/airfoil/details?airfoil=joukowsk0015-jf
http://www.airfoiltools.com/airfoil/details?airfoil=joukowsk0018-jf
Template from ASCEND! Team Lead Joseph Mena: Fall 2015 – Spring 2016

## Slide 18: Additional Pictures

## Slide 19: Extra Pics

## Slide 20: Principles Expanded (J – 18%)

## Slide 21: Principles Expanded (J – 15%)

## Slide 22: Principles Expanded (Eppler)

## Slide 23: The Payload
Testing controls systems as they pertain to balloon missions
Implementing passive design via aerodynamic stabilization in tandem with mass moment of inertia manipulation
Interested in:
  Stabilization effects for recording
  IMU (inertial measurement unit) data

## Slide 24: Payload Design (Dimensioning)

## Slide 25: Payload Design (Dimensioning)

## Slide 26: Payload Design
Ricoh Theta S
  360 Camera and Video support
  W/o external battery, picture every
  30 seconds for entire flight
  W/ external power, pictures every 10
  seconds with fully charged batteries
  Video capability only up to 25 minutes /
  4 GB until stop time
https://theta360.com/en/about/theta/s.html

## Slide 27: Final Payload – 2.942 lbs
ABS Main Chassis
4x PLA Outriggers
4x Zinc Threaded Rods
Ricoh Theta S – 360 Camera
Razor IMU – Accelerometer/ Gyroscope Readings
Carbon-Composite Bolting Board
Fiberglass Core Securing Rod
External Batteries