## Slide 1: Development of Unmanned Aerial Systems (UAS) for Planetary Analog Research
Connor Williams
Dr. Christopher Hamilton (Lunar and Planetary Laboratory)
Stephen Scheidt (Lunar and Planetary Laboratory)
26th Annual Arizona Space Grant Consortium Symposium
April 22, 2017

## Slide 2: Project
The goal of this project was to produce an unmanned aerial system (UAS) to study terrestrial environments that resemble Mars.
Required redesign of existing airframe to allow for portability to remote field sites.
Necessitated integration of a thermal infrared camera with a 3-axis gimbal.

## Slide 3: Components
VulcanUAV Hexacopter Airframe
Forward Looking Infrared Radiometer (FLIR) A65 Camera
Raspberry Pi 3 Microcomputer
3-Axis Gimbal
Control Equipment

## Slide 4: FLIR A65
Weight: 0.21 kg
IR Resolution: 640 x 512 pixels
Field of View: 25o x 20o
Data Transfer: Ethernet
Power Input: Ethernet
Source: FLIR Systems

## Slide 5
Source: FLIR Systems

## Slide 6: 3-Axis Gimbal
Assorted makes and models available.
Must be large enough to house both the FLIR and a visual spectrum camera.
Stabilizes camera and allows for targeting of specific formations on the fly.
Source: DJI

## Slide 7: Raspberry Pi 3
Dimensions: 85mm x 58.5mm
Ports:
    1x Ethernet
    4x USB
    1x HDMI
    1x Micro USB
Programming Language: Python
Weight: 23 grams
Source: Raspberry Pi

## Slide 8: Airframe
Configuration: Hexacopter
Construction Materials: Aluminum and Carbon Fiber
Motors: 6x KDE Direct 4215XF (1.84 HP each)
Propellers: 6x T-Motor 15” Carbon Fiber
Thrust: About 24 kg total
Electronic Speed Controllers:
6x KDE Direct UAS 75HV+

## Slide 9: Control Equipment
DJI WooKong-M Flight Controller
  Global Positioning System (GPS)
  Inertial Measurement Unit (IMU)
  Power Management Unit (PMU)
Spektrum DX9
  Transmitter
  Receiver
  Distributer

## Slide 10: Airframe Redesign
Requirement: Must be portable to remote field sites
(Example: Iceland).
Complete redesign of center plate was necessary.
Adjustable battery mount was installed.
Adjustable gimbal mount was installed.
Removable battery was installed.

## Slide 11: Center Plate

## Slide 12: Completed Center Plate

## Slide 13: Battery Tray and Gimbal Mount

## Slide 14: Mounted Battery

## Slide 15: Finished Product

## Slide 16: Future Activities
Selection of 3-axis aerial gimbal.
Integration of FLIR with gimbal and visual spectrum camera.
Programming of Raspberry Pi 3.
Installation of Amimon Connex HD video transmitter.

## Slide 17: Acknowledgements
Dr. Christopher Hamilton
Stephen Scheidt
University of Arizona Lunar and Planetary Laboratory
Arizona Space Grant Consortium

## Slide 18: Thank You