## Slide 1: Eye Movement Miscue Analysis: Building a low-cost software solution
26th Annual Arizona Space Grant Consortium Symposium
ASU, Phoenix, AZ
Shawtaroh (Shawn) Granzier-Nakajima, UA/NASA Space Grant
David Yaden, UA Prof. Language, Reading & Culture
April 22, 2017
Notes: 8-9 months

## Slide 2: Eye Movement Miscue Analysis (EMMA)
Towards a theory of reading
  Eye-Tracking during Read-Alouds
  Perception
    Oral Retellings
    Interview
      Probe about miscues
Commercial software doesn’t provide syncing of audio and visual files
Notes: simultaneous eye-tracking and audio-recording of oral-readings to understand readers’ patterns of visual attention to text and their their subsequent comprehension. Unfortunately, commercial eye-tracking software doesn’t provide syncing of audio and visual files, so equipment and software need to be tailored. “There is no firm definition for a fixation. It is less a physiological quantity than a method for categorizing sections of a data stream” (ASL, D7 Manual, p. 50) We use 50ms, 1.0° Visual Angle “We can often say that specific regions were ‘looked at,’ perhaps even fixated; however, we cannot be fully confident that these specific regions were fully perceived. ” (Duchowski, 2007, p. 209)

## Slide 3: Domain Analysis
ASL D6 Remote Tracker
Notes: We use 50ms, 1.0° Visual Angle

## Slide 5: Modifications
Hardware
  Secondary keyboard
    Page advancement tracked with XDAT markers
  Webcam & Speakers
    Record reader’s facial cues
    Captures reader’s oration
    Creates syncing markers
Software
  Batch and AutoHotkey Scripts
    Automates experimental setup, recording, analysis (Open Source libraries: ffmpeg, vlc, sox)

## Slide 6: Conclusions
Modular
Few keystrokes
Syncs audio and eye-movement files
Enables multi-page readings
Future
    Coloring Books
    July EMMA Conference
    Pharmacist Prescriptions

## Slide 7: Acknowledgements
David Yaden
Ken and Yetta Goodman
Kelly Allen
David Betts
NASA Space Grant
University of Arizona/ ASU

## Slide 8: Thank you