## Slide 1: PHOENIX COLLEGE
NASA ASCEND SYMPOSIUM PRESENTATION
2018-2019

## Slide 2
Eunice Lopez
Ivan Martinez
Jessica Frantz
Chris Yurgel
*Volunteers
Team Members
Modesta Juarez
Isai Uriarte*
Brian Moreno*
Jackie Salazar

## Slide 3
Livestream
In-flight Video
Build Protective Lightweight Housing
Gather Atmospheric Data
2018-2019 Main Goals

## Slide 4
Video System
APRS Packet
APRS Server
Rotor
Controller Software
Video Transmission Software
Video Transmission
Payload
Rotor System
Livestream!

## Slide 5
  Hardware
  Raspberry Pi Camera
  Raspberry Pi
  Ubiquiti Rocket M5AC Wireless Transceiver
  5.8GHz Dipole Wi-Fi Antennas
  Software
  Linux
  FFmpeg
Video System on Payload

## Slide 6
Raspberry Pi
• Linux OS
• Video Processing
Raspberry Pi Cam
• 720ppi
• 24FPS
Rocket M5
• Ubiquiti Air Os
• Video Transmission
Video Processing on Payload

## Slide 7
Ground Station Video System
  Hardware
  Ubiquiti Rocket M5AC Wireless Transceiver
  Ubiquiti 5.8GHz Rocketdish-LW Series Dish Antenna
  Software
  VLC Player
  OBS Screen Capture

## Slide 8
Rocket M5
• Ubiquiti Air Os
• Video Reception
Video Processing
• VLC
• OBS
YouTube
• Livestream video
RocketDish
• 30dBi
Video Processing on Ground Station

## Slide 9
  Hardware
  Ubiquiti Rocket M5AC Wireless Transceiver
  LSM303 for heading
  9-DoF for elevation
  BU-353S4 GPS
  HS-805MG 5:1 Servo gearboxes
  Software
  Arduino
  Python
Ground Station Tracking System

## Slide 10
Arduino
• Ground station position data processing
• Data comparison and feedback
Servos
• Antenna positioning
APRS Server
• Automatic packet reporting system data from the payload
GPS
• Ground station coordinates
Python Scripts
• Location data processing
Ground Station Tracking System

## Slide 11
Video System Results
  Achieved a video connection for 20.8 miles
  Achieved a data connection for 21.5 miles
  Slight delay in video stream
  Successfully rotated our dish antenna based on APRS packets (Fall 2018)
  Managed to control our dish antenna based on manually inputted coordinates determined from APRS packets (Spring 2019)

## Slide 13
Lightweight carbon fiber housing protects electronic components and allows secure mounting
Kevlar cord suspension method reduces weight
Ease of access to on/off switch and LED power indicators
Housing and Suspension

## Slide 14
Atmospheric Profiling System
External temperature sensor – DS18B20
Orientation sensors – MPU6050 and LSM303
Barometer – MPL3115A2
MicroSD card breakout board
Arduino prototype shield
Arduino Uno

## Slide 15
Atmospheric Profiling System
Chart: External Temperature
Chart: Accelerometer
Chart: Internal Temperature
Based on the logged data, we were able to determine loss of power when our payload reached minimum temperatures.
Power resumed during descent

## Slide 16
Lightweight power solution for all subsystems
Reduced points of failure by eliminating unnecessary components and wiring
Includes data transfer line from raspberry pi to Ubiquiti modem.
Primary components:
7.4V LiPo Battery
Buck/Boost for 5V line
Step-Up voltage regulator for 12V line
Power and Data Distribution Board
RJ45
RJ45
5V
12V
7.4V
Ubiquiti
Modem
Raspberry Pi
Data
Atmospheric Transmission System
Raspberry Pi

## Slide 17: Thank you!
Special Acknowledgements:
Arizona Space Grant Consortium
Arizona Near Space Research
Ernest Villicaña (Faculty Mentor)
Dr. Ed Ong (Science Advisor)