## Slide 1
Communications Subsystem (Comms)
Austin Macosky – Communications Subsystem Lead

## Slide 2: Outline
Mission Overview
  Responsibilities
  Data requirements and abilities
  Passes per day and orbit
  Link Budget
System Overview
  Important requirements
  Communication system overview
  Uplink encryption and station licensing
Subsystem Design
  Satellite
  Ground Station

## Slide 3: Mission Overview
Uplink:
  OBC – Commands for bus systems and payloads
  Transceiver – Reconfiguration in orbit
Downlink:
  OBC – Compiled health and science data

## Slide 4: Orbit and Passes Per Day
System designed for ISS orbit
  400-435 km
  16 orbits per day
  >3 usable passes per day on average

## Slide 5: ISS Passes > 10° For 10 days
Fig COMM-1: 10-day Visibility Forecast

## Slide 6: Data Requirements
Subsystem | Data/Cycle | Cycles/Day | Data/Day
CRP | 8 kB | 16 | 128 kB
MDE | 8 kB | 16 | 128 kB
OBC | 8 kB | 4 | 32 kB
Total Data Per Day
288 kB

## Slide 7: Data Capabilities
Data rate | Data per 3-minute pass | Data per day (8 minutes)
19.2 kbps | 432 kB | 1.15 MB
100 kbps | 2.25 MB | 6 MB
  Total data for uplink and downlink combined

## Slide 8: Link Budget
NIST Communications Group Link Budget Calculator

## Slide 9: System Overview
USB 3
Coax
Coax
UART
Ground Station Computer
Ground Station Transceiver
Ground Station Antenna
Satellite Antenna
Satellite Transceiver
Onboard Computer
Fig COMM-7: System Communication Diagram

## Slide 10: Station Licensing
FCC Part 97.207 (f) "Space telemetry transmissions may consist of specially coded messages intended to facilitate communications or related to the function of the spacecraft."
  Verified 'specially coded' = encrypted
FCC Part 97.211 (b) "A telecommand station may transmit special codes intended to obscure the meaning of telecommand messages to the station in space operation."
These sections apply if:
  The space station is located more than 50 km above the Earth's surface (FCC Part 97.3(41))
  The data being downlinked is "measuring instruments in a spacecraft including those related to the functioning" (FCC Part 97.3 (42)
  The transmissions are coming from an 'amateur station that transmits communications to a space station (FCC Part 97.3(45)

## Slide 11: Station Licensing
FCC Part 97.313 "An Earth station or telecommand station, however, may transmit on the 435-438 MHz segment with a maximum of 611 W effective radiated power (1 kW equivalent isotropically radiated power) without the authorization otherwise required. The transmitting antenna elevation angle between the lower half-power (?3 dB relative to the peak or antenna bore sight) point and the horizon must always be greater than 10°".
We will be applying for a station power waiver if necessary
  Granted for ES1 (may be frequency specific)

## Slide 12: IARU Frequency Coordination
Frequency coordination request will be submitted to both the FCC and IARU
Current issues
  Other CubeSats have had launches scrubbed due to frequency coordination issues
  Government power struggle over frequency coordination
  Cannot complete paperwork until manifested

## Slide 13: EnduroSat UHF Transceiver Type II
Configurable data rate
  19.2 kbps
  100 kbps
1-Watt RF output
Transparent protocol
  Allows custom packet format
High sensitivity receiver –121dBm
Spectrally efficient 2GFSK modulation
94 g
Software updates and reconfiguration in orbit
Fig COMM-8: UHF Transceiver Type II

## Slide 14: EnduroSat UHF Antenna
Circularly polarized dipole array
  Rejects reflected signals
1.1dBi maximum gain
-2dBi minimum gain
  Acceptable omnidirectional backup performance
Antenna deployment feedback
Thin enough to mount below -z crossmember
500 mA deployment current
Isolated burn circuit for each element
Backup burn resistor for each element
Fig COMM-9: UHF Antenna

## Slide 15: Subsystem Design (Ground Station)
RF HamDesign Satellite Ground Station Kit
  4.5m parabolic dish
    24dbi gain @ 435 MHz
    10.5 degree –3dB beam width
  BIG-RAS azimuth and elevation rotator
    Dishes up to 5m
    0.5-degree resolution
  MD-02 rotator controller
    1-degree resolution
    Emulates Yeasu products (compatibility)
  Custom multiband feed point
    Primary band 435Mhz
    LMR600 coax
  High-speed desktop
    DSP using GNU Radio
Fig COMM-11: AxFab Antenna

## Slide 16: Ground Station Transceiver
LimeSDR Mini
  Maximum 30.72 MSPS
  Full duplex
  Frequency range: 10 Mhz – 3.5Ghz
  12 bit DAC
  SMA connectors
  USB 3.0
  DSP with GNU Radio
    Allows for high data throughput
    Cataloging & capturing passes
Fig COMM-12: LimeSDR Mini

## Slide 17: GNU Radio
Downlink
  Capture raw waveform of pass
  Demodulate downlinked data
  Catalog and store pass data autonomously
Uplink
  Interface with satellite control GUI
  Modulate commands
  Doppler shift correction
  Transmit
Fig COMM-16: GNU Radio Logo

## Slide 18: Questions?
Austin Macosky
MacoskyA@my.erau.edu