## Slide 1
Evaluation of Threshold Friction Velocities at Potential Dust Sources in Semi-Arid Regions
Arizona Space Grant Symposium 2020
HAS Superfund Laboratory
Presenter: Ruby O’Brien-Metzger
Mentors: Dr. Eric Betterton, Dr. Eduardo Saez, Kyle Rine
Funded By: NIEHS Superfund Research Program, NASA Space Grant Program

## Slide 2
Friction Velocity
  Shear stress at the surface
  Mechanical erosion
Threshold Friction Velocity
  Friction velocity that is needed for mechanical erosion
  uf
Log-Wind Profile
  uz: Wind speed at height Z
  κ: Von Kármán constant (0.4)
  zo: Roughness length
  u*: Friction velocity
z
uz
u*
zo
Theory

## Slide 3
Portable Dust Generator
Based on PI-SWERL by DRI
Produces a known wind speed
Measures real time dust production
Lightweight and Compact
1. Exhaust Tube 2.Blower 3.Adjustable legs 4.Hall Sensor 5.Annular Ring 6.Isokinetic Sampling Port 7.Motor 8.Adjustable Skirt

## Slide 4
Chart: Dust and Wind Speed in Picacho Peak

## Slide 5
Traditional Wind Tunnel
Portable Dust Generator
Lower Cost
Lower maintenance
Less labor required
Smaller foot print
Ease of use
Photo Credit: Desert Research Institute

## Slide 6
Effect of Atmospheric Relative Humidity
Soil moisture and relative humidity.
The Biosphere 2, humidity controlled environments.
Reproducible test surface.

## Slide 7
Effect of Atmospheric Relative Humidity

## Slide 8
Erodible Potential of Surfaces
The potential for a dust storm can depend on presence of aerosolizable particles.
Recent wind activity.
Crusting/disturbance of the surface.
On Crusted surfaces
After the initial run, Threshold Friction Velocity values increased past the detection limit of our instrument.
On Disturbed surfaces
Threshold Friction Velocity values remained constant through successive runs.