## Slide 1: Predicting satellite-to-ground propagation effects induced by the Ionosphere
Joshua Smith
Mentor : Dr. Mike Parker
Rincon Research Corporation
April 18, 2020
Virtual symposium

## Slide 2: CatSat
The University of Arizona is launching a 6U CubeSat called CatSat in the Spring of 2021
One hurdle Cat-Sat will face is dealing with Ionospheric propagation effects
Statement of the problem;
CatSat’s orbit is projected to near 550 km
Source: https://uanews.arizona.edu/story/ua-studentled-catsat-mission-selected-nasa
Notes: Statement of the problem;
CatSat’s orbit is projected to near 550 km

## Slide 3: The Problem with The Ionosphere
Statement of the problem;
The Ionosphere contains high concentration of electrons that can effect signals passing through it.
Source: https://spotlight.unavco.org/how-gps-works/gps-basics/gps-and-geosciences.html

## Slide 4: Objectives: Predicting Propagation Effects
For CatSat’s mission, it would be very helpful to predict these effects induced by the Ionosphere
  Number of Faraday Rotations
  Time Delay/ Total Slant Electron Content
  Changes in Frequency

## Slide 5: Input: Satellites Orbit path, frequency, Vertical TEC, Ground Station coordinates,
Group delay
Number of Rotations
United States, Congress, Klobuchar, John A. “Ionospheric Effects on Earth-Space Propagation.”
Ionospheric Effects on Earth-Space Propagation.
Notes: Using equations obtained from John A Kolobuchar paper Total elctron Content studies,
I wrote C code that allows you to input given coordinates for a ground station, Vertical Total Electron content, a salatites postion Data optained form a SPG module
To produce Group delay/Slant Total electron and number of faraday rotations for passes over that ground station, given the satalites transmitting at 100 MegaHertz

## Slide 6: Main Assumptions
  Nonvarying Vertical Total Electron Content
  Thin shell for the Ionosphere at an Altitude of 400 Km
  Spherical Model of the Earth
  Dipole Model of the Earths Magnetic
  Ray Paths are not being Bent or refracted by the Ionosphere
Notes: Using equations obtained from John A Kolobuchar paper Total elctron Content studies,
I wrote C code that allows you to input given coordinates for a ground station, Vertical Total Electron content, a salatites postion Data optained form a SPG module
To produce Group delay/Slant Total electron and number of faraday rotations for passes over that ground station, given the satalites transmitting at 100 MegaHertz

## Slide 7: Test Case Input
Let’s Say CatSat has an Orbit altitude near 550 km
Has an orbit path similar to Landsat-7
The Vertical TEC = 10^18 electrons/m^2
Transmitting at f = 100 MHZ
Ground station is at Lat: 32 Long: -111 (Tucson)

## Slide 8: Test Case Expectations (Not To Scale)
GD
CatSat
CatSat
VTEC = 10E18 el/m^2
Ionosphere
STEC>VTEC
Line of Sight

## Slide 9: Test Case Expectations (Not To Scale)
GD
CatSat
CatSat
Magnetic Field Vectors
CatSat
Magnetic North
Pole

## Slide 10: Elevation angle (degrees) Vs Time (Ksec)

## Slide 11: Elevation angle (degrees) Vs Time (Ksec)

## Slide 12: Results

## Slide 14: Results

## Slide 15: Why These Predictions are Important
  Number of Faraday Rotations
    If we measure fading amplitude, when our model suggests it should be higher, could suggest something has happened (i.e. Spinning)
  Time Delay
    Can Give us a better understanding of how the Ionosphere behaves
  Changes in Frequency
    Transmitter needs to tuned to the same frequency being received
Notes: Interpretations of these predictions
Match how STEC should increase at the horizons and reach a minuim when directly above the GD
Matches the behavior of how Faraday rotation should reverse in direction for this high pass
Skeptical about magnitude of FR
Don’t know actual TEC, it can vary greatly but we can measure the # of faraday Rotations
Worst case scenario
Model can tell us if something is wrong

## Slide 16: Conclusion/Future work
Predictions seem to match behavior of our expectations
Possible Problems with magnitude for FR
Future work
  Integrate code into Rincon Research’s X-midas server
  Finish coding for the induced change in Frequency
  Enhance Code so that it reflects more realistic situations (i.e. Magnetic field)

## Slide 17: Acknowledgements
Thank you so much to….
Dr. Mike Parker
Rincon Research
David Chan
Michelle Coe
Arizona Space Grant Consortium

## Slide 18: Thank You!!