## Slide 1: UNDERWATER EXPLORATION DRONE
RODNEY STAGGERS JR (ARIZONA STATE UNIVERSITY)
MENTORED BY PROF. JNANESHWAR DAS

## Slide 2: ABSTRACT
This project is centered on crafting an autonomous underwater vehicle (AUV) to aid human divers that are proposed to take in-depth images of coral reefs

## Slide 3: INTRODUCTION
Causes of Coral Reef Deaths
  Increased UV exposure
  Ocean level temperatures
  Toxic runoff

## Slide 4: LIMITATIONS OF STRATEGY AND PROPOSED SOLUTION
Aerial spectrometer & DPVs
Limited number of experts
Costly Logistics
  DPV’s cost is +$10,000
  Room for casualties
Drone Requirements
  Cost effective (<$10,000)
  Go up to 30m below the surface
  Stay within 1m of coral
  Autonomously map and image
DPV (Diver Propulsion Vehicle)

## Slide 5: EVOLUTION OF THE FRAME
V1 V2 V3
Notes:   Internal frame had to be able to hold
    Two Lithium-Ion Batteries
    Pixhawk Flight Controller
    Stereolab ZED2 and FLIR/Point Grey Chameleon 3 Cameras
    Jetson TX2
    Sufficient space for potential add-ons

## Slide 6: RESULTS
  CAD Simulations for Hydrostatic pressure
    At 30m, the max. pressure is 302.8kPa gage
    (A) is the sensor mount and (B) is the motor mount

## Slide 7: EQUATIONS OF MOTION
  M: rigid body structure (mass and inertia tensors)
  C(v): Coriolis effect and centripetal forces and moments
  D(v): drag forces and moments (neglected for simplicity)
  g(η): gravity, buoyancy, and moments about the center of gravity
  τ: vector of input forces and moments (from thrusters and current)
X
Z
Y

## Slide 8: STATE OF MOTION
η is the vector of position and orientation
v is the vector of angular velocities (u, v, w) and angular accelerations (p, q, r)

## Slide 9: COMPARISON TO CURRENT MODELS
Seabotix
Bluefin-21 (Typical AUVs)
Unlike typical AUVs, it has multi-rotor thrusters
Able to retain memory and coordinate movement
Full range of motion (no sawtooth pattern)
Notes:   This same application can be applied to Space Exploration
  Multi-rotor thrusters
  No or little gravity as well as drag
  Hovering or Drifting, turning in place, ROV have tether or inspection
  UAV: turbines (one thruster/fin w/sawtooth)
    Navy

## Slide 10: DISCUSSION
Application for Space Exploration
  Ability to deploy over an area and navigate
  Similarities between drone and a rocket
    Modified dynamics can be used to adapt to non-terrestrial exploration

## Slide 11: CONCLUSIONS
Final Cost: $4000
  Test the VIO when immersed underwater
  Manufacture an updated drone
Upcoming Plans:

## Slide 12: ACKNOWLEDGEMENTS
Thanks to the NASA Space Grant Consortium, the D.R.E.A.M.S. LAB, Prof. Jnaneshwar Das, Alex Goldman, Cole Brauer, and Harish Anand for their guidance and collaboration.

## Slide 13: REFERENCES
https://www.google.com/url?sa=i&url=https%3A%2F%2Fgiphy.com%2Fexplore%2Fgreat-coral-reef&psig=AOvVaw0f_w9xH9qNe2H6aQ9bxm6_&ust=1585893093988000&source=images&cd=vfe&ved=0CA0QjhxqFwoTCIDFsqeGyegCFQAAAAAdAAAAABAD
https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.pbs.org%2Fnewshour%2Fscience%2Fhow-global-warming-is-permanently-reshaping-the-great-barrier-reef&psig=AOvVaw1S2ZRi0EtHN9lHs30gj_Sw&ust=1585858868385000&source=images&cd=vfe&ved=0CA0QjhxqFwoTCMCMy6SHyOgCFQAAAAAdAAAAABAD
Mantha, Maitreyi. “Back-To-Back Mass Bleaching Decimates Australia's Great Barrier Reef.” DOGOnews, DOGO Media, Inc., 03 Jun, 2017, www.dogonews.com/2017/6/3/back-to-back-mass-bleaching-decimates-australias-great-barrier-reef.
https://www.naval-technology.com/wp-content/uploads/sites/5/2017/09/LBV200-4-rov1.jpg
https://robots.ieee.org/robots/aqua/Photos/SD/aqua-photo1-full.jpg
https://www.naval-technology.com/projects/bluefin-sandshark-micro-autonomous-underwater-vehicle/
Fossen, Thor I., Handbook of Marine Craft Hydrodynamics and Motion Control, First Edition. 2011, John Wiley & Sons Ltd.