## Slide 1: UArizona ASCEND: Profiling High-Altitude Radiation with a General Data Logger
Speakers:
Nick Blanchard, Kevin May, Daniel McConville
University of Arizona ASCEND Launch Fall & Spring

## Slide 2: Agenda
Introduction
Fall launch and details
Spring launch and details
Lessons learned

## Slide 3: Fall Launch
In flight
Launch
Landing
Notes: Investigations
  Verification of electronics design for atmospheric data collection
  Preliminary data future radiation shielding experiments
  New videography method
Failure
  Wiring
    Housing design poor for wire management, led to damage

## Slide 4: Spring Launch
Notes: Investigations
  Again...verification of electronics design for atmospheric data collection
  Preliminary data future radiation shielding experiments
  New housing design to fit all components inside

## Slide 5: Housing Design
Fall Housing
3D Printed (PLA)
12x12x12cm
  GoPro & Geiger counters mounted on exterior
Spring Housing
3D Printed (PLA)
1U Standard CubeSat (10x10x10cm)
  All components inside — most compact design yet
  GoPro views through polycarbonate window
Housing
Drawer
Complete
Complete
Design
Notes: Fall housing
Interior dedicated to electronics
  Unable to use PCB designed in Spring since a part specified from Spring was no longer available in Fall
    Required impromptu wiring which made failure far more likely
  Drawer contained batteries and electronics
    Temperature, pressure, humidity, radio components
  Top-mounted geiger counters (2X)
  Side mounted, exterior GoPro
    “Time warp” mode in 4k resolution
Successful video capture (despite only ~45 minutes) and radio transmitter function
Spring housing
Interior desiccated to fit everything
  PCB allowed for better fitment
  1 3-cell LiPo, 1 2-cell LiPo
  GoPro with polycarbonate window
  Initially intending to run GoPro from main batteries
    Voltage issue prevented camera from working properly
    Decided to run at lower resolution and framerate to preserve battery life in retail GoPro battery
Since Fall failed with data collection, this presentation focuses on the Spring payload

## Slide 6: Electronics (Spring Payload)
Component | Purpose
Adafruit Metro Mini (ATMega328) | Microcontroller
Adafruit BME 680 (I2C) | Atmospheric Profiler
Adafruit MMA 8451 (I2C) | 3-Axis Accelerometer
RadiationWatch Pocket Geiger | Radiation Measurements
Adafruit MicroSD Card Module (SPI) | Datalogging
Adafruit Powerboost 1000c | Power Delivery
11000 mAh LiPo | Power Storage
Status LED | Display System Status
Notes: Mention changes from Fall payload

## Slide 7: Schematic and PCB

## Slide 8: Spring Data + Conclusions

## Slide 9: Atmospheric Data

## Slide 10: Radiation Intensity Data
95% Confidence Interval for Beta (Slope):
7.367*10^-5 < Beta < 8.5864*10^-5

## Slide 11: Interpretation of Radiation Data
(Phillips 2016)
Notes: Case can be made for a low-cost, safe radiation test bench

## Slide 12: Spring Launch Video Screenshots

## Slide 13: Thank You Arizona Near Space Research Arizona Space Grant Consortium Michelle Coe Radiation Reference: Dr. Tony Phillips, “Intercontinental Space Weather Balloon Network” https://spaceweatherarchive.com/2016/11/05/intercontinental-space-weather-balloon-network/
arizonaseds@gmail.com
www.seds.arizona.edu