## Slide 1: ERAU ASCEND 2021 Arizona space Grant symposium | April 17, 2021

## Slide 2: TEAM
Members
Nicodemus Phaklides – Team Lead
Zach Howe – Integration Lead
Michael Lauber – Structures Lead
Mentor
Dr. Douglas Isenberg

## Slide 3: Payload Overview
Goals:
Study heat transfer within a high-altitude balloon payload
Develop a thermally stable, modular system that future experiments can be based on
Resolve attitude and position for the payload in flight
Record video of flight

## Slide 4: HEAT TRANSFER Experiment
26 thermistors are used to measure temperature around the craft
Two temperature sensors on the board
  IMU and Altimeter
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25

## Slide 5: ADDITIONAL EXPERIMENTS
Position Resolution:
  Adafruit MTK3339 GPS
Adafruit MPL3115A2 Barometric Altimeter
Attitude Resolution:
  Adafruit BNO055 Absolute Orientation IMU
  External Solar Panels routed into ADC
A GoPro will be used to record video of the flight

## Slide 6: Results
Failures:
GoPro battery was not charged enough to record inflight video
Microcontroller rebooted 3 times in flight
  57,000ft - peak - 46,000ft, 43,000ft – 24,000ft, 1,600ft
GPS could not achieve lock until landed
Successes:
Heat transfer experiment recorded excellent data
IMU and Altimeter data recorded nominally
Payload and all components recovered safely without damage
Image Credit: Xander Pickard

## Slide 7: Heat transfer CONGLOMERATED results
Top Exterior
Bottom Exterior
Interior Sensors

## Slide 8: Heat transfer experiment results

## Slide 9: IMU accelerometer Data

## Slide 10: Points of failure
This meant that an exterior power supply module had to be incorporated
A capacitor on the power supply blew up during testing, rendering the entire module inoperable.
External power supply had to be routed into the pin header, inherently flimsy connection.

## Slide 11: Conclusion
Overall, the payload was a success
Heat Transfer Experiment yielded good results
  With enough insulation, active heating is not required
  A lack of atmosphere for convection allows payloads to heat up near space
    Cooling solutions are more important to focus on (high-altitude and recovery)
Failures have given important insights on
  Payload structure design
  PCB design
  Integration
  Testing

## Slide 12: SPECIAL THANKS
Mentor
Dr. Douglas Isenberg
Ground Support:
Xander Pickard
Jack Crabtree
ASNR

## Slide 13: Thank you!

## Slide 14: ELECTRONICS and software
The payload uses a BeagleBone Green as its microcontroller
A custom PCB cape handles all of the sensors
  32 analog inputs are condensed via two 16:1 MUXs into AIN0 and AIN1 of the BeagleBone
  Adafruit sensors communicate via UART/I2C
Software is written in Python 3
  Main loop saves all sensor data to a 32GB SD-Card every second

## Slide 15: STRUCTURE
10 in by 10 in foam box
  2.616lb
Thermal vent on side to cool payload when landed
  Servo pulls a hole in the side
  The servo is set to go off when altitude hasn’t changed and T>4hr
GoPro is imbedded into the foam
Solar panels are glued onto the exterior
Lid is attached by Velcro and nut