## Slide 1
Space Environment Radiation Testing
On Electrical Components
Mairely Urias, Dr. Hugh Barnaby
Arizona State Univeristy
School of Electrical, Computer, and Energy Engineering
2023 Arizona/NASA Space Grant Symposium
April 22, 2023

## Slide 2
SPACE RADIATION
Sources:
O1
O2
O3
Particles trapped in Earth's magnetic field
Solar particle events
Galactic cosmic rays
Radiation: Energy that is emmited in the form of rays, electromagnetic waves, and/or particles
Space Radiation: made up of atoms in which electrons have been stripped away as atoms accelerate in interstellar space to speeds approaching the speed of light, Ionizing Radiation

## Slide 3
RADIATION EFFECTS IN ELECTRONICS
Upsets/Anomalies:
  Loss of data
  Spurious signals
  Phantom commands
  Performance degradation
  Single Event Effects (SEE) in microelectronics:
    1101 0101
  Electromagnetic pulses
  Range from transient, cumulative, permanent, recoverable, or destructive
SYSTEM FAILURE

## Slide 4
SINGLE EVENT EFFECTS
TOTAL IONIZING DOSE
  Individual incidents
  Single highly energetic particle
  Soft errors:
    Non-destructive, bit flips, logic transients
  Hard errors
    Permanent functional effects
    May or may not be destructive
  Latch-ups, burnouts, gate ruptures
  Cumulative, long term
  Caused by all ionizing radiation sources
  Performance degradation
  Potentially leads to failure over time
  Voltage shifts, leakage currents, gain degradation

## Slide 5
ANALOG FAILURES
DIGITAL FAILURES
POWER FAILURES
CODE/ALGORITHM FAILURES
  Code Corruption
  Power Control Malfunctions
  Memory Corruption
  Soft Errors
    1101 0101
  Performance Degradation
  Operational Failures

## Slide 6
Measure radiation effects & failure mechanisms
RADIATION HARDENING BY DESIGN
Identify failure mechanisms
Identify radiation effects responsible
Use knowledge to improve design
O1
O2
O3
O4
GOALS
  INCREASE RELIABILITY
  REDUCE/ELIMINATE SUSCEPTIBILITY TO FAILURE MECHANISMS
  INCREASE LIFESPAN

## Slide 7
DEVELOPING A TEST INTERFACE
Selected DUT:
LM741 Operational Amplifier
  General purpose, commonly used as noninverting
  Overload protection on input and output
  No latch-up when range is exceeded
Radiation Source:
Hitachi ProBeat IV Synchotron-based pencil beam scanning system at Mayo Clinic, Phoenix, AZ

## Slide 8
DEVELOPING A TEST INTERFACE, CONT.
Circuit Analysis
Simulation:
LTSpice

## Slide 9
DEVELOPING A TEST INTERFACE, CONT.
Testing Parameters:
SRIM
Testing Configurations:
Arduino
Configuration #1 : (000)
Switch 1: LOW Exp. Output:
Switch 2: LOW -4.226 V
Switch 3: LOW
Configuration #2 : (100)
Switch 1: HIGH Exp. Output:
Switch 2: LOW -0.425 V
Switch 3: LOW
Configuration #3 : (011)
Switch 1: LOW Exp. Output:
Switch 2: HIGH -0.570 V
Switch 3: HIGH
September 2022
•200 MeV protons
•5mm beam diameter
•90% uniformity
•Measurement Points (Fluence) :
•Post 5 x 10^11 cm-2
•Post 2.5 x 10^12 cm-2
November 2022
•200 MeV protons
•5mm beam diameter
•90% uniformity
•Measurement Points (Fluence) :
•Post 1 x 10^12 cm-2
•Post 5 x 10^12 cm-2
Linear Energy Transfer (LET): energy deposited per unit track length, normalized to density (MeV-cm2)
Total Ionizing Dose (TID): measure of energy absorbed by a unit mass per matter, or rad, by ionizing radiation.

## Slide 10
DEVELOPING A TEST INTERFACE, CONT.
PCB Design:
KiCad

## Slide 11
TEST RESULTS
SEPTEMBER RESULTS
NOVEMBER RESULTS
  Consistent with long-term radiation Total Ionizing Dose (TID) effects
  Deleterious to device operation

## Slide 12
DATA INTERPRETATION
  Data shows damage prolonged radiation exposure can cause in LM741
  Changes in input bias current affect performance:
    Increased power consumption
    Inaccurate output readings
  Continued testing important for safety and reliability of space missions

## Slide 13
VERSION 2
  Multi-DUT
    Linear Bipolar Circuits
    MOS
    Diodes
    FPGA
  More parameter data
    Slew Rate
    Temperature
    Voltage Range
  Multi-use

## Slide 14
Questions?

## Slide 15
Acknowledgments
A special thanks to :
  Dr. Hugh Barnaby, for the guidance and mentorship
  Dr. Daniel Robertson and the Radiation Oncology Research Committee at the Mayo Clinic for allowing and facilitating the use of proton beam for academic use
  ASU/NASA Space Grant Consortium