## Slide 1: Digital Analysis of Ionospheric Plasma On-board Waves, Instabilities & Noise Spectrometer (WINS)
Ahmad Qureshi
Advised By:
Naomi Yescas

## Slide 2: Waves, Instabilities & Noise Spectrometer (WINS)
WINS is a specialized instrument to be deployed on a CubeSat,
It can delve into the intricacies of the ionosphere by collecting and analyzing electrostatic waves.
Focused on measuring ionospheric plasma at magnetohydrodynamic scales.

## Slide 3: What I Did As Part Of WINS

## Slide 4: ABOUT MY PROJECT
I created a new Fast Fourier Transform (FFT) and programmed it onto an FPGA board
I took the concept from an idea, to an algorithm, to novel digital hardware
I did a lot of learning along the way!

## Slide 5: Understand FFTs Create Algorithm Approach Create Hardware
I spent time understanding the FFT and its application in research
I created an algorithm that did a FFT in C
I spent a lot of time converting the C to a Verilog/Hardware Implementation

## Slide 6: Windowing is taking the data and multiplying it by some value to avoid any one data point from affecting any other data point Fourier Analysis: Windowing

## Slide 7: Fourier Analysis: Post-Windowing
In creating an unsigned integer transform, all data had to be converted to positive.
This moved negative numbers to be low and positive numbers to be high.
This is the same data!

## Slide 8: Signed Data Unsigned Data Output Data - CPU

## Slide 9: Hardware Implementation: Block Diagram

## Slide 10
Hardware Implementation: Block Diagram

## Slide 11: PYNQ Board Implementation
Yellow pins are wired to create my prototype Fourier Transform Circuit!

## Slide 12: Max Latency: 8.75 ns 114 MHz Final FFT Statistics
Power Utilization:
1.7 Watts

## Slide 13: Next Steps
Run test data through the prototype and test the FFT
Create an ASIC that completes the same thing as the hardware on the FPGA
Place the created ASIC on a larger PCB
Test, test, test!

## Slide 14: Acknowledgements
Thank you to these great people!
My PI, Mihailo Martinovic
My mentor, Naomi Yescas
My fellow intern in the lab, Sarina Blanchard

## Slide 15: Thank You!

## Slide 16: Cyclotron Motion Since our data has small time, we assume the motion is linear and reject all Cyclotron motion. We can make this assumption since the relevant waves are damped